Porting RIOT OS to the RioT-Board
by Lennart Dührsen and Leon George

---
RioT-Board

---
RioT-Board
- Introduced by Freescale Semiconductor in early 2014
- Based on the i.MX6Solo Application Processor
- Ships with Android installed, Linux (Ubuntu) also available
- Costs ca. 70€
- Low Energy Consumption (if you don't charge your phone using the USB-Ports :-) ), although quite powerful

---
RioT-Board

---
RioT-Board
CPU:
- i.MX6Solo
- ARM Cortex-A9 (32Bit)
- 1GHz, Single Core
- 32 KByte L1 Instruction Cache
- 32 KByte L1 Data Cache
- 512 KB unified I/D L2 cache
- Private Timer and Watchdog

---
RioT-Board
Memory:
- Boot ROM 96KB
- Internal RAM 144KB
- DDR3 RAM 1GB

---
RioT-Board
Interfaces:
- 3 Pin Debug Port (UART)
- JTAG
- USB (4x Host, 1x OTG)
- 10MBit/100MBit/1GBit Ethernet
- GPIO Expansion Port
- I²C

---
RioT-Board
What to do with it?
- Suitable for many tasks, including
  - Personal Computer
  - Multimedia-Station (XBMC)
  - Small Server
  - …
But what about IoT?

---
RIoT-Board
1. Adding some sort of wireless Transceiver/Receiver
2. (and sensors maybe), it could be
- Part of a typical sensor network (you'd need an
  AC-Adaptor or a really strong battery)
- A Router (Home-Wifi, AODV, OLSR, RPL...)
- Central instance of a sensor network that collects
  all the data and processes it
- ...

---
RIOT-OS
2. ...well you know about RIOT, obviously ;-)
4. But the question is: How to port it?

---
RIOT-OS
- Operating Systems are (mostly) written in C
- Most parts are hardware generic
- But some have to be written exactly for the underlying metal!
- e.g. the booting process, context switch, timer etc.

---
RIOT-OS
1. #include "irq.h"
2. #include <stdio.h>
3. #include "kernel_internal.h"
5. extern void board_init(void);
7. __attribute__((constructor)) static void startup(void)
8. {
9. /* use putchar so the linker links it in: */
10. putchar('\n');
12. board_init();
14. puts("RIOT MSP430 hardware initialization complete.\n");
16. kernel_init();
17. }

---
RIOT-OS
To get RIOT to run, the following has to work:
- UART I/O for debugging and shell communication
- Timer(s) so the kernel can run
- Interrupts
- Set up a stack
- Build it successfully (probably the hardest part :-) )

---
Strategy
- Read documentation
- Read more documentation
- Adjust folder structure and create Makefiles
- Split work in an ad hoc way, as soon as
  we know what we're doing

---
Strategy
3. Good luck to ourselfes, thank you for listening!